## Slide 1: Frost Protected Shallow Foundations
Jay H. Crandell, P.E.
ARES Consulting/ABTG

## Slide 3: Overview
History & Code Acceptance
Principles
Cost Savings
Technology Verification
Applications
Construction Method
IRC 2006 Requirements
Plan Review & Inspection Checklist
Beyond the IRC: ASCE Standard 32-01
Resources & References
Conclusions

## Slide 4: History of FPSFs
1930s – Frank Loyd Wright designed and built the first FPSFs in the Chicago area
1950s – 1970s In rebuilding after WWII, Scandinavian countries studied U.S. construction and then became leaders in FPSF technology
1980s – U.S. Plastics Industry and NAHB/RC begin technology transfer back to U.S.
1992 -1994 U.S. HUD sponsors a 5-home verification study in the northern U.S. climates; Air-freezing Index map is created; U.S. design guide developed
1995 CABO OTFDC – first model code recognition of FPSF in U.S.
2001 – ASCE standard 32 is completed (based on HUD guides for FPSFs)

## Slide 5: Code Acceptance
2000/2003/2006 – IRC includes simplified FPSF provisions for homes
2003/2006 – ASCE standard 32-01 referenced in IRC and IBC for residential and commercial building applications
Market Acceptance:
>1,000,000 in Scandinavia (and continuing)
1,000s in U.S. (and growing)

## Slide 6: Cost & Energy Savings
Construction cost savings: $1,000 to $4,000 (depends on size and complexity of foundation and severity of local frost depth/climate)
Compared to basement construction, the cost savings more than double.
Annual energy savings: ~$75 per year (typical 6,000 HDD heating climate)
FPSF insulation amount can be sized to also meet or exceed Energy Code
FSPF insulation can be increased to improve slab comfort; works great with in-slab heating systems
TIP: Not necessarily cost-effective for unheated building foundations
Aren’t these
numbers exciting!

## Slide 7: Principles
Frost Depth in Ground
Heat Transfer & Storage
Heat Loss at Corners
Two Approaches, Same Principles
The “Frost-Heave Triangle”

## Slide 8: Frost Depth in Ground

## Slide 9: Heat Transfer & Storage

## Slide 10: Heat Loss at Corners (3D)
3D heat transfer at outside corners is greater than 2D heat transfer along wall

## Slide 11: Two Approaches, Same Principles
Heated Buildings (living spaces conditioned ≥ 64o F):

## Slide 12: Two Approaches, Same Principles
Unheated Buildings (unconditioned <41oF)

## Slide 13: The Frost-Heave Triangle
All of the following must occur for frost heave to happen:
Freezing Temperatures
Moving Into Soil
Frost-Susceptible Soil Type (e.g., silt)
Wet Soil Condition
(e.g., >75% saturation)

## Slide 14: FPSF Technology Verification
Sponsored by U.S. Dept. of Housing and Urban Development (1992-1995)
Built and monitored 5 homes in VT, IA, ND, and AK
Used dataloggers and 90 +/- thermocouples in foundation and ground to monitor temperatures and frost line at building and “far-field”.
Monitored for 2 complete years and winter events
Some foundation portions designed for only average winter freezing temperatures to simulate the 100-year event

## Slide 15: Test Site #1 – Williston, VT

## Slide 16: Test Site #1 - Results

## Slide 17: Test Site #2 – Spirit Lake, IA

## Slide 18: Test Site #2 - Results
Key:
Outdoor
Indoor
Ground @ 21” depth
Subgrade at corner
Subgrade at garage corner
Slab surface, 3’ from edge
Period of Record:
11/20/92 to 4/20/94

## Slide 19: Test Site #3 – Fargo, ND

## Slide 20: Test Site #3 - Results

## Slide 21: Test Site #4 – Palmer, AK

## Slide 22: Test Site #4 - Results

## Slide 23: Test Site #5 – Fargo, ND

## Slide 24: Test Site #5 - Results

## Slide 25: Demonstration Projects
DOE / NREL (House in Colorado)
DOE Build America (various)
HUD/PATH Demonstrations (various)
Others?

## Slide 26: FPSF Applications
Residential Buildings & Additions
Commercial Buildings
Infrastructure (U/G utilities, roads, dams, retaining walls, etc.)

## Slide 27: Applications: Slab on Ground (Heated Building)*
Monolithic thickened edge
Concrete stem wall
Permanent wood stem wall
CMU stem wall
* Recognized in IRC 2000/2003/2006

## Slide 28: Applications: Unvented Crawlspaces (Heated Building)*
* Unvented crawlspaces recognized in 2006 IRC Section R408.3. But, FPSF insulation must be determined in accordance with ASCE 32-01 (referenced in IRC and IBC)

## Slide 29: Applications: Walk-out Basement (Heated Building)*
Apply FPSF insulation to exterior of basement wall, or
Use Permanent wood walls (insulation in wall)
* Not addressed in IRC; must refer to ASCE 32

## Slide 30: Applications: Unheated Buildings*
Ground insulation must “blanket” entire footprint of foundation
Also used for unheated
portions of heated buildings
* Must refer to ASCE 32 to size insulation and selection insulation type to support light structural loads

## Slide 31: Applications: Unheated “Cold” Foundations*
* Refer to ASCE 32 (not addressed in IRC)

## Slide 32: Applications: Exterior Slabs/Stairs, Retaining Walls, U/G Wet Utilities*
*Not addressed in IRC or ASCE 32 – refer to Norwegian guidelines
Utility Trench
Exterior Stairway
Retaining Wall

## Slide 33: Construction Method (Monolithic SOG)
Form slab using vertical foam and cast slab
Place drain pipe (if horizontal insulation used)
Use concrete truck to place pea-gravel aggregate around foundation
Place horizontal insulation on smooth gravel surface
Protect vertical insulation (to 6” below grade)
Protect horizontal insulation if required and extends more than 24” from face of foundation
Backfill with loader

## Slide 34: Construction Method (Plastic Lumber Stem Wall & SOG)
Insulation Protection
Electric Utility Rough-in

## Slide 35: 2006 IRC Requirements for FPSFs
SCOPE: heated building slab-on-grade foundations only–for other applications refer to ASCE 32.
STEP 1: Determine AFI per Figure R403.3(2)
STEP 2: Specify and size FPSF insulation per Figure R403.3(1) and Table R403.3*
STEP 3: Details
  Joining to heated or unheated foundations (R403.3.1)
  Protection of insulation (R403.3.2)
  Drainage (R403.3.3)
  Termite protection (R403.3.4)
*Only XPS and EPS insulation materials listed in Table R403.3(2) and complying with ASTM C578 are permitted for FPSF construction

## Slide 36: Example Problem: Lincoln, NE
STEP 1: 100-yr AFI = ~1,500 oF-days
Figure R403.3(2) Air-Freezing Index
Estimate of the 100-Year Return Period
For AFI by local weather stations, refer to http://lwf.ncdc.noaa.gov/oa/fpsf

## Slide 37: Example Problem: Lincoln, NE
Table R403.3
Minimum Insulation Requirements for Frost-Protected Footings in Heated Buildings
STEP 2: To determine insulation thickness, divide required R-value by effective R-per-inch values (for below ground service) in footnote ‘c’ of Table R403.2
R-req’d = 4.5
Eff. R/in = 3.2
(Type IX EPS)
Thickness =
4.5R / 3.2R/in
= 1.4” (use 1.5”)
Or
Eff.R/in = 4.5
(Type IV XPS)
Thickness =
4.5R / 4.5R/in
= 1.0”

## Slide 38: Example Problem: Lincoln, NE
STEP 3: Details (Foundation wall cross section)
Figure R403.3(1)
Insulation Placement for Frost-Protected Footings in Heated Buildings

## Slide 39: Example Problem: Lincoln, NE
STEP 3: Details (Foundation Insulation Plan)
Figure R403.3(1)
Insulation Placement for Frost-Protected Footings in Heated Buildings
(NOT REQUIRED)

## Slide 40: Special Conditions
IRC 403.3.1.1 – Unheated building conventional foundation (e.g., garage) adjoining an FPSF foundation (e.g., house); shows insulation at interface of foundations
IRC 403.3.1.2 – FPSF foundation (e.g., addition) adjoining a conventional heated building foundation (e.g., existing house)

## Slide 41: Additional Requirements
Figure R403.3(1) – Vertical insulation must be protected against physical damage and U/V radiation from top of foundation to 6” below grade (various options such as trt’d plywood, elastomeric coatings, stucco, etc.)
Section R403.3.2 – Horizontal insulation must be protected if less than 12” below grade or when extending outward more than 24”

## Slide 42: Additional Requirements
R403.3.3 – Drainage layer and drain to daylight required under horizontal insulation; slope finish grade to drain away from building
R403.3.4 – provide termite protection per R320.5*
*Per Section R320.5, foundation wall insulation must be terminated above ground to allow a minimum 6” inspection strip in areas with “heavy” termite infestation probability. This inspection strip is not permitted with FPSF (creates a thermal short circuit). Therefore, recommend using foam impregnated with termiticide in “heavy” areas.

## Slide 43: Verify FPSF Insulation Meets Energy Code
2006 IRC Chapter 11, Table N1102.1 requires R10 slab edge insulation, 2’ wide (Climate Zone 5)
FPSF design for Lincoln, NE requires 1.0” of nominal 5 R/in XPS which gives 1.0” x 5 R/in = 5.0R (or 1.5” EPS x 4.2 R/in = R6.3, nominal) << R10
Now What?
(1) increase FPSF thickness to meet energy code (or use IECC energy code trade-off), or
(2) Use DOE Building Foundation Design Handbook (Table 4-1) to show that using 2’ of R5 insulation on the exterior face of the foundation (FPSF design) saves more energy than using 2’ or R10 insulation placed horizontally under the slab as permitted by the energy code.

## Slide 44: Plan Review and Inspection Checklist
 Insulation type (per ASTM C578)
 Insulation dimensions and continuity
 Foundation depths
 Distance from top of slab to grade
 Protection of insulation
 Termite precautions
 Drainage

## Slide 45: Overview of ASCE 32
Provides for three different building use conditions (heated, semi-heated, and unheated)
Provides insulation requirements for slab on grade, crawlspace, and basement foundations.
Provides insulation requirements for isolated footings or small unheated areas of otherwise heated buildings
Allows horizontal (wing) insulation to be reduced in size in trade-off with increasing minimum foundation depth
Provides guidance for use of non-frost susceptible fills
Future edition may include a risk-consistent frost depth map for conventional foundations correlated to the AFI map in the IRC and ASCE 32 based on work by Cornell University and NOAA. For example, Lincoln, NE (AFI = 1,500 oF-days) would have a design frost depth of 32” – not very different than current practice of 36” – southern U.S. and seaboard states will be affected more by this change.
…..ASCE 32 is a reference standard in the 2003/2006 IRC and IBC and is applicable to foundation and building types addressed in the IRC and IBC.

## Slide 46: Resources and References
IRC 2006 (www.iccsafe.org)
IBC 2006 (www.iccsafe.org)
Revised Builder’s Guide to FPSFs (www.toolbase.org or www.nahb.org)
Various FPSF research reports and older design guides (www.huduser.org)
ASCE Standard 32-10 (www.asce.org)

## Slide 47: Conclusions
$1,000-$4,000 cost savings per home/business
$75/yr energy savings
Long history of successful performance
Easy to design
Easy to build
Easy to inspect
Any questions?