## Slide 1: Window Installation Methods for Frame Walls with Foam Sheathing
Revised 6/30/2021
Notes: Change title and presenter info to suit purpose.

## Slide 2
Copyright © 2021 Applied Building Technology Group
Applied Building Technology Group (ABTG) is committed to using sound science and generally accepted engineering practice to develop research supporting the reliable design and installation of foam sheathing. ABTG’s educational program work with respect to foam sheathing is supported by the Foam Sheathing Committee (FSC) of the American Chemistry Council.
ABTG is a professional engineering firm, an approved source as defined in Chapter 2 and independent as defined in Chapter 17 of the IBC.
DISCLAIMER: While reasonable effort has been made to ensure the accuracy of the information presented, the actual design, suitability and use of this information for any particular application is the responsibility of the user. Where used in the design of buildings, the design, suitability and use of this information for any particular building is the responsibility of the Owner or the Owner’s authorized agent.
Foam sheathing research reports, code compliance documents, educational programs and best practices can be found at www.continuousinsulation.org.

## Slide 3: Outline
Background
Key Principles
Scope
Applicability
Installation Details
Installation Steps

## Slide 4: Background
There are many acceptable ways to mount and detail windows for support and weather resistance.
This presentation covers representative solutions for integrating windows with Foam Plastic Insulating Sheathing (FPIS).
It is the responsibility of the user to verify the appropriateness of any specific detail for their specific conditions.

## Slide 5: Key Principles
The intent of any acceptable detail for integrating windows with FPIS is:
  To provide adequate structural support to the window unit.
  To prevent water penetration at the window-wall interface by flashing to direct water onto the exterior surface of the WRB layer and/or cladding and away from the window opening.
  Ensure the detail is consistent with or meets the intent of window, flashing, and WRB manufacturers’ installation instructions.

## Slide 6: Scope
Four installation methods are featured in this presentation
Other wall components not shown include:
  Cladding (various types)
  Structural sheathing (if required for bracing)
  Interior finish (e.g., gypsum wallboard)
  Vapor retarder (various types or “classes” as required by code)
Window Buck
Standard
Rainscreen (furred siding)
Picture Frame

## Slide 7: Applicability
The “standard” method is traditionally used for FPIS up to 1-1/2” thick and windows not more than 6’ wide
The “picture frame” method is used where additional window support is needed and with FPIS of ¾” to 1-1/2” thick to match typical 1x or 2x lumber thickness
The “window buck“ method also is used where additional window support is needed and usually when the FPIS is over 1-1/2” thick.
The “rainscreen” method is used with rainscreen (furred) cladding installation.

## Slide 8: Applicability
The installation methods featured in the presentation assume use of windows with integral mounting flanges (i.e., nail fin).
  Although, some methods (like the window buck and picture frame methods) are relevant to “block frame” windows without a flange
Fasteners are installed through the pre-punched holes in the flange and flashing and sealants are applied to the flange during installation
  Be sure that the flange fastener length is increased to accommodate the thickness of FPIS when using the “standard” installation method.

## Slide 9: Applicability
Similar installation methods can be used for flanged door installations
  Thresholds should always have full support (e.g., blocking equal to thickness of FPIS – similar to that used for the “picture frame” method)
  Where frame/hinge anchors are required into rough opening framing, in-swing exterior doors generally allow for FPIS thickness of up to 1-1/2 inches. Beyond that, use of a “window buck” is recommended.
    Outswing exterior doors generally require use of a “window buck” where FPIS thickness exceeds 1”

## Slide 10: Applicability
FPIS materials comply with the following standards:
  Expanded Polystyrene (EPS) - ASTM C578,
  Extruded Polystyrene (XPS) - ASTM C578, or
  Polyisocyanurate (Polyiso) - ASTM C1289
Where the window flange bears directly on FPIS, the FPIS must have a minimum compressive strength of 15 psi per the above standards (equivalent to 2,160 PSF bearing capacity).

## Slide 11: Applicability
The installation methods featured in this presentation assume use of FPIS as a water-resistive-barrier (WRB) system.
  Refer to DrJ DRR 1410-05 for a listing of FPIS manufacturers with code-approved FPIS WRB systems and installation instructions.
  Use of a separate WRB material layer is also common and acceptable with appropriate installation and detailing.

## Slide 12: Applicability
Use flashing materials and sealants recommended by the window, FPIS, and/or WRB manufacturers.
Flexible adhered flashing is featured in this presentation, but fluid-applied flashings also may be used in similar fashion.
Follow sealant and flashing manufacturer’s instructions to ensure adhesion and durability.

## Slide 13: Installation Details
Ordered by installation method:
  Sill details
  Jamb details
  Head details

## Slide 14: Standard Method – Sill Detail

## Slide 15: Standard Method – Jamb Detail

## Slide 16: Standard Method – Head Detail

## Slide 17: Window Buck – Sill Detail

## Slide 18: Window Buck – Jamb Detail

## Slide 19: Window Buck – Head Detail

## Slide 20: Window Buck – Plywood Buck (alternative to 2x lumber buck)
https://www.nist.gov/system/files/nzertf-architectural-plans3-june2011.pdf
https://www1.eere.energy.gov/buildings/publications/pdfs/building_america/incorporating-thick-layers-exterior-insulation.pdf

## Slide 21: Picture Frame – Sill Detail

## Slide 22: Picture Frame – Jamb Detail

## Slide 23: Picture Frame – Head Detail

## Slide 24: Rainscreen Method – Sill Detail

## Slide 25: Rainscreen Method – Jamb Detail

## Slide 26: Rainscreen Method – Head Detail

## Slide 27: Basic Installation Steps
The following installation steps are based on the “standard” method
Similar steps apply to the other installation methods (see previous detail differences).
For a printable installation instructions refer to CI’s Quick Guide on Window Installation.

## Slide 28: STEP 1: Frame Window Opening
Frame walls with wood or steel as required by the applicable code.
Ensure window rough opening is square and plumb and of the size required for the window.
  If using the “window buck” method, frame the buck into the rough opening or be sure to leave extra clearance for the buck to be installed after framing to accommodate the required window rough opening size.
Top plate
Header
Sill plate
Wall stud
Cripple stud
Bottom plate

## Slide 29: STEP 2: Install FPIS
Follow FPIS manufacturer’s installation instructions
If an FPIS WRB system, install flashing and joint sealing materials per manufacturer’s instructions
  Where a separate WRB is used, following the WRB manufacturer’s installation instructions

## Slide 30: STEP 3: Install Sill Pan Flashing
Pan flashing is a recommended best practice and is required by some manufacturer’s instructions.
Apply flashing or sill pan component in accordance with manufacturer’s instructions.
Sloped sill is recommended, especially if sealant to window frame is used as the backdam (see STEP 8).

## Slide 31: STEP 4: Install Rough Opening Jamb and Head Flashings
Recommended best practice for continuous air-barrier between wall and window.
Sometimes required or recommended by manufacturer’s instructions.
Shingle lap jamb flashing over sill flashing and head flashing over jamb flashing

## Slide 32: STEP 5: Install Window
Follow window manufacturer’s instructions for flange fastening, support (e.g., shims), and additional anchorage if required (e.g., frame fasteners or brackets).
Use flange fasteners of sufficient length to penetrate FPIS and framing
Apply bedding sealant under flange per manufacturer’s instructions
  Omit at sill flange for drainage if using a sill pan

## Slide 33: STEP 6: Install External Jamb Flashings
Follow flashing manufacturer’s instructions for proper application

## Slide 34: STEP 7: Install External Head Flashing
Follow flashing manufacturer’s instructions for proper application
Where flexible adhered flashing is used, a best practice is to apply “termination tape” over the top edge of the adhered flashing for extra protection
  FPIS WRB joint tape is often used for this purpose

## Slide 35: Step 8: Apply Sealant
Air seal window around entire perimeter on the interior with sealant or low-expanding foam made for this purpose.

## Slide 36: Additional Resources
For additional window installation resources refer to:
  Window Installation Application page
  CI’s Quick Guide on Window Installation
  ABTG Research Report 2104-01 – Installation & Performance of Flanged Fenestration Units Mounted on Walls with FPIS
  Window Installation Details for Effective Sealing Practice (from the National Research Council of Canada)
  Window Sill Details for Effective Drainage of Water (from the National Research Council of Canada)
Always use product manufacturer’s installation instructions as the primary resource!
Notes: Additional reading
36